## Slide 1: Chap 12 Power Amplifiers

## Slide 2: 12.1 General Considerations
High voltage stress if directly powering the load
  Example: 1 W to 50-Ω load
    Amplitude=10 V, peak voltage=20 V (Swing from 0-20 V)
    It is impossible in a CMOS device.

## Slide 3: 12.1 General Considerations
High Peak Current
  20 V/50Ω=400 mA (possible by increasing the size)

## Slide 4: 12.1 General Considerations
Matching Network
  Trading high current for high voltage
  1 V dc supply to power 1 W output
  Vpp=2 V, 4 A peak current.
Figure 12.3. (a) Impedance transformation by a matching network, (b) realization by a transformer.

## Slide 5: Effect of high current
Increase the size of transistor to accommodate high current
Increase the input capacitance
Large driving power is needed

## Slide 6: Effect of high current
Large voltage drop on bonding wire
  Example: 0->4A at 1 GHz
  if the voltage drop across this inductance must remain below 100 mV?
This is an extremely small inductance. (A single bond wire’s inductance typically exceeds 1 nH.)

## Slide 7: Efficiency
Drain efficiency
Power-Added Efficiency

## Slide 8: Linearity
Nonlinearity
  high adjacent channel power as a result of spectral regrowth
  amplitude compression
The PA characterization begins with two generic tests of nonlinearity based on unmodulated tones:
  intermodulation and compression.
  yielding a first-order estimate of the PA nonlinearity

## Slide 9: AM/AM and AM/PM conversion

## Slide 10: Single-Ended and Differential PAs
Most stand-alone PAs have been designed as a cascade of single-ended stages. Two reasons account for this choice:
  the antenna is typically single-ended,
  and single-ended RF circuits are much simpler to test than their differential counterparts.
Drawbacks
  First, they “waste” half of the transmitter voltage gain
  Large current induced feedback

## Slide 11: Single-Ended and Differential PAs

## Slide 12: Single-Ended and Differential PAs
Suppose a given balun design has a loss of 1.5 dB. In which one of the transmitters shown in Figs. 12.8(b) and 12.10 does this loss affect the efficiency more adversely?
30 dBm output compared to 0 dBm input
300 mW compared to 0.3 mW

## Slide 13: 12.2 Classification of PAs
Class A Pas
  η=50%
  1) The device can withstand 2 VDD
  2) Nonlinearity is tolerable
  3) Passives are lossless

## Slide 14
Explain why low-gain output stages suffer from a more severe efficiency-linearity trade-off.
Saturation discipline

## Slide 15: Efficiency boosting for class-A PAs
(1) the supply voltage and bias current remain at the levels necessary for full output power and only the input signal swing is reduced
Output power
DC supply power

## Slide 16: Efficiency boosting for class-A PAs
(2) the supply voltage remains unchanged but the bias current is reduced in proportion to the output voltage swing

## Slide 17: Efficiency boosting for class-A PAs
(3) both the supply voltage and the bias current are reduced in proportion to the output voltage swing.
Always keeping

## Slide 18
A student attempts to construct an output stage with a variable supply voltage as shown in Fig. 12.14. Can this circuit achieve an efficiency of 50%?

## Slide 19: Class B PAs

## Slide 20: Class C PAs

## Slide 21: 12.3 High-efficiency PAs
Class A stage with harmonic enhancement

## Slide 22: Class A stage with harmonic enhancement

## Slide 23: Class-E stage

## Slide 24: Class-F Power Amplifiers

## Slide 25: Cascode output stages

## Slide 26: 12.5 Large-signal Impedance Matching
a nonlinear complex output impedance must be matched to a linear load.

## Slide 27
The key point here is that maximum power transfer does not correspond to maximum efficiency.

## Slide 28: Load-pull Measurement
Figure 12.36. (a) Load-pull test, (b) contours used in load-pull test, (c) computation of input and output matching impedances.

## Slide 29: 12.6 Basic Linearization Tech.
Feedfoward

## Slide 31: Cartesian Feedback

## Slide 32: Predistortion

## Slide 33: Envelope Feedback

## Slide 34
Figure 12.45. (a) Mixer as envelope detector, (b) source follower as envelope detector, (c) limiter and mixer as envelope detector, (d) realization of (c).

## Slide 35: 12.7 Polar Modulation

## Slide 36
Figure 12.49. (a) Partial realization of EER, (b) output stage with envelope-controlled load, (c) local envelope feedback.

## Slide 37: Issues
1. Time mismatch
The corruption is therefore proportional to the derivative of the envelope signal, leading to substantial spectral regrowth
For example, in an EDGE system, a delay mismatch of 40 ns allows only 5 dB
of margin between the output spectrum and the required spectral mask

## Slide 38: Issues
1. Time mismatch
  The problem of delay mismatch is a serious one because the two paths in Fig. 12.46 employ different types of circuits operating at vastly different frequencies:
  the envelope path contains an envelope detector and a low-frequency buffer, whereas the phase path includes a limiter and an output stage.

## Slide 39: Issues
2. Linearity of the envelope detector
3. A nonlinear circuit having a finite bandwidth introduces AM/PM conversion
  Thus, the limiter in Fig. 12.46 may corrupt the phase signal by the large excursions in the envelope.

## Slide 40: Issues
4. AM/PM conversion due to output capacitance nonlinearity

## Slide 41: Polar Modulation
Figure 12.52. Polar modulation using baseband signal separation and (a) a VCO, or (b) a quadrature upconverter.

## Slide 42: Polar Modulation

## Slide 43: Polar Modulation

## Slide 44: Polar Modulation

## Slide 45: Polar Modulation
Figure 12.59. Phase signal leakage path.

## Slide 46: 12.8 Outphasing

## Slide 48: Issues
1. the gain and phase mismatches between the two paths result in spectral regrowth at the output
The last two terms on the right-hand side create spectral growth because they exhibit a much larger bandwidth than the composite
signal (the first term).

## Slide 49: Issues
2. the required phase bandwidth of each path
3. the interaction between the two PAs through the output summing device.
the load seen by one PA is modulated by the other and hence varies with time, distorting the signal.

## Slide 50: Issues
3. the interaction between the two PAs through the output summing device.
cot

## Slide 51: Issues
The dependence of Z1 and Z2 upon θ reveals that, if the PAs are not ideal voltage buffers, then the signal experiences a time varying voltage division and hence distortion

## Slide 52
addition of a constant inductance and a constant capacitance to the
output nodes provides only a rough compensation

## Slide 53
Figure 12.65. (a) Outphasing PA using Chireix’s technique, (b) addition of variable capacitances, (c) circuit with discrete
capacitor arrays.
if ΔC varies in proportion to sin 2θ, then the cancellation is more accurate

## Slide 54: Doherty Power Amplifier

## Slide 56: Design Example

## Slide 57: Design Example
1. The use of a cascode device affords nearly twice the drain voltage swing (compared to a simple common-source stage)
2. The matching network need only transform 50 Ω to about 4.4 Ω for an output power of 1 W, exhibiting smaller losses.
3. The on-resistance of the M1–M2 branch is chosen to be about 1.2 Ω, smaller than other equivalent resistances in the matching network, but requiring a W/L of 15 mm/0.25 μm for each
4. The large drain capacitance of M2 is absorbed in C1, and the gate capacitance of M1 is tuned by a 2-nH bond wire and an external variable capacitance. Inductors L2 and L3 are also realized by bond wires.