## Slide 1: Chap 7 Passive Devices

## Slide 2: 7.1 General Considerations
Modern RF design needs many inductors.
Example: Disadvantages
  (a) the bandwidth at node X is limited to 1/[(RD‖rO1)CD],
  and (b) the voltage headroom trades with the voltage gain, gm1(RD ‖ rO1).
CMOS technology scaling tends to improve the former but at the cost of the latter. For example, in 65-nm technology with a 1-V supply, the circuit provides a bandwidth of several gigahertz but a voltage gain in the range of 3 to 4.
little dc voltage drop, the circuit can comfortably operate with low supply voltages while providing a reasonable voltage gain (e.g., 10).

## Slide 3: 7.1 General Considerations
In addition to cost penalties, the use of off-chip devices entails other complications
  Significant coupling
  Significant parasitics at higher frequencies

## Slide 4: 7.1 General Considerations
Identify two undesirable coupling mechanisms if the LO inductor is placed off-chip.

## Slide 5: 7.1 General Considerations
Modeling Issues
  inductors and some other structures are much more difficult to model.
  In fact, the required modeling effort proves a high barrier to entry into RF design:
    one cannot add an inductor to a circuit without an accurate model,
    and the model heavily depends on the geometry, the layout, and the technology’s metal layers (which is the thickest).

## Slide 6: 7.2 Inductors
Basic structure
  Owing to the mutual coupling between every two turns, spirals exhibit a higher inductance than a straight line having the same length.
  To minimize the series resistance and the parasitic capacitance, the spiral is implemented in the top metal layer (which is the thickest).

## Slide 7
A two-dimensional square spiral is fully specified by four quantities (Fig. 7.5): the outer dimension, Dout, the line width, W, the line spacing, S, and the number of turns, N.
The inductance primarily depends on the number of turns and the diameter of each turn, but the line width and spacing indirectly affect these two parameters.

## Slide 8
Example 7.3.
The line width of a spiral is doubled to reduce its resistance; Dout, S, and N remain constant. How does the inductance change?
the doubling of the width inevitably decreases the diameter of the inner turns, thus lowering their inductance, and the larger spacing between the legs reduces their mutual coupling. We note that further increase in W may also lead to fewer turns, reducing the inductance.

## Slide 9
Compared with transistors and resistors, inductors typically have much greater dimensions (“foot prints”), resulting in a large chip
area and long interconnects traveling from one block to another. It is therefore desirable to minimize the outer dimensions of inductors.
the line resistance rises, degrading the inductor quality
the mutual coupling between the sides
of the innermost turns reduces the inductance

## Slide 10
Relevant to typical inductor designs is the plot for a line length of 20 μm, suggesting that a diameter of 5 to 6 times W should be chosen for the inner opening to ensure negligible coupling. It is helpful to remember this rule of thumb.

## Slide 11: 7.2.2 Inductor Geometries

## Slide 12: 7.2.3 Inductance Equations
For example, an empirical formula that has less than 10% error for inductors in the range of 5 to 50 nH is given in [1] and can be reduced to the following form for a square spiral:
where Am is the metal area (the shaded area in Fig. 7.5) and Atot is the total inductor area ( in Fig. 7.5). All units are metric.

## Slide 13
An interesting property of inductors is that, for a given wire length, width, and spacing, their inductance is a weak function of the number of turns.

## Slide 14
For example, if ltot = 2000 μm, W = 4 μm, and S = 0.5 μm, then as N varies from 2 to 3 to 4 to 5, then inductance rises from 3.96 nH to 4.47 nH to 4.83 nH to 4.96 nH, respectively.
In other words, a given length of wire yields roughly a constant inductance regardless of how it is “wound.”
The key point here is that, since this length has a given series resistance (at low frequencies), the choice of N only mildly affects the Q (but can save area).
But the number of turns must be at least 2 to create mutual coupling.

## Slide 16: Accuracy Considerations
The above inductance equations yield different levels of accuracy for different geometries. For example, the measurements on tens of inductors in [3] reveal that Eqs. (7.19) and (7.20) incur an error of about 8% for 20% of the inductors and an error of about 4% for 50% of the inductors.
For a resonator, we must determine the tolerable error in ω0.
Field simulations are necessary
  Equations can only be applied to initial design

## Slide 17: 7.2.4 Parasitic Capcitances

## Slide 20: 7.2.5 Loss Mechanisms
Metal Resistance
For example, a 5-nH inductor operating at 5 GHz with an RS of 15.7 Ω has a Q of 10.

## Slide 21
Unfortunately, the above example portrays an optimistic picture: the Q is limited not only by the (low-frequency) series resistance
but also by several other mechanisms. That is, the overall Q may fall quite short of 10.
As a rule of thumb, we strive to design inductors such that the low-frequency metal resistance yields a Q about twice the desired value, anticipating that other mechanisms drop the Q by a factor of 2.

## Slide 22
RS falls to a relatively constant value for N > 3.
for a given W, S, and wire length, the inductance is a weak function of N. Thus, with W and S known, a desired inductance value translates to a certain length and hence a certain dc resistance almost regardless of the choice of N.

## Slide 23
In summary, for a given inductance value, the choice of N has little effect on RS, and a larger W reduces RS to some extent but at the cost of higher capacitance.

## Slide 24: Skin effect

## Slide 25: Eddy current

## Slide 26: Eddy current
Current crowding also alters the inductance and capacitance of spiral geometries.

## Slide 27: Capacitive Coupling to Substrate

## Slide 28: Magnetic Coupling to the Substrate

## Slide 29: 7.2.6 Inductor Modeling

## Slide 30: 7.2.6 Inductor Modeling

## Slide 31: 7.2.6 Inductor Modeling

## Slide 32: 7.2.7 Alternative Inductor Structures

## Slide 33: 7.2.7 Alternative Inductor Structures

## Slide 34: 7.2.7 Alternative Inductor Structures

## Slide 35: Inductors with Gound Shield
We now observe that the shield can provide a low-resistance termination for electric field lines even if it is not continuous. As illustrated in Fig. 7.44 [13], a “patterned” shield, i.e., a plane broken periodically in the direction perpendicular to the flow of eddy currents, receives most of the electric field lines without reducing the inductance. A small fraction of the field lines sneak through the gaps in the shield and terminate on the lossy substrate. Thus, the width of the gaps must be minimized

## Slide 36: Stacked Inductors

## Slide 37: 7.3 Transformers

## Slide 38: 7.3 Transformers

## Slide 39: 7.3 Transformers

## Slide 40: 7.3 Transformers

## Slide 41: 7.3 Transformers

## Slide 42: 7.4 Transmission lines

## Slide 43: 7.4 Transmission lines

## Slide 44: 7.4 Transmission lines

## Slide 45: 7.4 Transmission lines

## Slide 46: 7.4 Transmission lines

## Slide 47: 7.5 Varactors

## Slide 48: 7.5 Varactors

## Slide 50: 7.6 Constant Capacitors
MOS Capacitors
  Advantages:
    the highest density in integrated circuits because Cox is larger than other capacitances in CMOS processes.
  Disadvantages
    First, to provide the maximum capacitance, the device requires a VGS higher than the threshold voltage
    Second, the channel resistance limits the Q of MOS capacitors at high frequencies.
    Nonlinearity

## Slide 51: 7.6 Constant Capacitors
Metal-Plate Capacitors
  The Q and linearity of well-designed parallel-plate capacitors are typically high
  Less capacitance density than MOSFET
    with nine metal layers in 65-nm technology,
    1.4 fF/μm2 compared to 17 fF/μm2.

## Slide 52: 7.6 Constant Capacitors
Metal-Plate Capacitors